https://pubs.rsc.org/en/content/articlelanding/2017/cs/c6cs00066e#!divAbstract

M-47

#17
 4.1.2. Non-thermal plasmas

In its simplest way,

 a non-thermal plasma is created by applying a potential difference between two parallel electrodes,

 which are inserted in a reactor filled with gas (or they form the reactor walls).

#17.0.1
 This potential difference creates an electric field,

 which causes so-called gas breakdown,

 i.

e. the gas ‘breaks up’ (to some extent) into positive ions and electrons,

 although the majority of the gas molecules still remain neutral.

#17.0.2
 The electrons are accelerated by this electric field towards the positive electrode (anode).

 When they collide with gas molecules,

 it can give rise to ionization,

 excitation and dissociation.

#17.0.3
 The ionization collisions create new electrons and ions; the ions are accelerated by the electric field towards the negative electrode (cathode),

 where they cause secondary electron emission.

 The new electrons – created by ionization or secondary electron emission at the cathode – can then further give rise to further ionization collisions.

#17.0.4
 These processes make the plasma self-sustaining.

 The excitation collisions create excited molecules,

 which can decay to the ground-state (or another lower level),

 thereby emitting light,

 which is one of the characteristic features of plasmas.

#17.1
 Finally,

 the dissociation collisions create radicals,

 which can easily form new compounds,

 and this forms the basis of the gas conversion applications of non-thermal plasmas.

#17.1.1

Although this way of plasma creation,

 i.

e. by applying a potential difference between two electrodes,

 is #%only one possibility to create a plasma,

 the principle of gas activation by electrons,

 creating reactive species (ions,

 excited species,

 radicals) is equally valid for other types of plasmas as well,

 and will be discussed in Section 4.2 below.

#17.1.2
 In general,

 this gas activation by electrons is also the reason for the good energy efficiency of CO2 conversion by non-thermal plasmas,

 as will be explained below.

#17.1.2
In non-thermal plasmas,

 the electrons are indeed characterized by a much higher temperature than the heavy particles,

 leading to the non-LTE condition,

 as mentioned above.

 As a result of all the different species,

 the relationship between all their different temperatures can become quite complex,

 but conventionally the temperature of the electrons (Te) is the highest,

 followed by the vibrationally excited molecules (Tv),

 while the lowest temperature is shared by the neutral species (T0, or simply the gas temperature,

 Tg),

 the ions (Ti) and the rotational degrees of freedom of the molecules (Tr); hence the temperature order is: Te ≫ Tv > Tr ≈ Ti ≈ T0.21

In most cases, the electron temperature is in the order of 1 eV (∼10 000 K),

 while the gas temperature remains close to room temperature.

 This high electron temperature is due to the small mass of the electrons,

 allowing them to be easily accelerated by the applied electromagnetic fields,

 whereas the heavy particles – even the ions – are not easily accelerated.

#17.1.3
 Furthermore,

 due to the large mass difference,

 the electrons lose less energy during elastic collisions with heavy particles,

 so they can easily keep their high energy gained from the electric field.

#17.1.4
As mentioned above,

 the electrons can be considered as the initiators of the highly reactive chemical mixture.

 This is obviously one of the key advantages of non-thermal plasma technology: it allows gases – even as unreactive as CO2 – to be ‘activated’ at room temperature by the highly energetic electrons.

#17.1.4
 Accordingly,

 there is no need to heat the entire reactor or the gas,

 because the discharge and the associated reactions are easily initiated by applying an electromagnetic field.

#17.1.5
 This results in the second key advantage of non-thermal plasma technology for CO2 conversion,

 namely that it is a very flexible,

 or so-called turnkey,

 process,

 since it can easily and,

 more importantly,

 instantaneously be switched on and off,

 with conversion and product yield stabilization times generally lower than 30 minutes.

#17.1.6
 Furthermore,

 its power consumption can easily be scaled and adjusted.

 As such,

 it has the inherent ability to be(come) one of the most suitable technologies to utilize excess intermittent renewable energy (e.

g. energy originating from wind turbines or solar panels) and for storing it in a chemical form.

 Indeed,

 this makes it suitable for both peak shaving and,

 more importantly,

 grid stabilization,

 by being able to adapt to the irregular supply of renewable electricity.

#17.2
 Hence,

 in essence the current transition to renewable energy sources not only gives plasma processes a clean electricity source,

 but plasma-based CO2 conversion technology can also provide a solution for the imbalance between energy supply and demand by enabling the storage of electrical energy in a desirable chemical form according to the market needs.

#17.2.1
Additional advantages compared to the other emerging technologies for CO2 conversion are the low investment cost for the reactors,

 as they do not rely on rare earth materials,

 and last but not least,

 their simple scalability from watt to megawatt applications,

 as already demonstrated by the successful development of ozone generators.

80

#17.2.2
Due to their extreme scalability,

 the applications can vary hugely in both scale and application type,

 starting from small devices,

 such as on board vehicles for exhaust treatment or to provide on board fuel cell feeds81 as well as in household-scale devices for indoor air treatment,

82,83 to medium on-demand installations,

 such as modular containerized plant concepts84 or in in situ CO production,

85 and finally to large-scale industrial plants.

 This scalability and flexibility in applications also gives plasma technology a high #%locational flexibility.

 As such,

 both production on demand and remote production become possible,

 which is a critical point for %%carbon capture and utilization (CCU) techniques.

#17.3
On the other hand,

 for the comparison made here with other novel technologies,

 the reliance of non-thermal plasma technology on indirect solar energy in the form of electricity is at the same time a limiting factor for the overall solar-to-fuel conversion efficiency,

 compared to technologies that can harvest solar energy in a direct form.

#17.3.1
 However,

 when looking at the broader picture,

 its ability to rely on multiple energy sources again gives plasma technology a huge advantage regarding locational flexibility,

 not to mention that it can be operated 24/7, even when the sun is not shining.

#17.3.2
Although non-thermal plasma is good at creating a non-equilibrium condition by ‘activating’ stable molecules,

 it is absolutely #%non-selective in the formation of targeted products.

 More specifically,

 the reactive species created by the electrons react according to the laws of chemical kinetics,

 and as such,

 they recombine into a (large) number of different products,

 depending on the reaction conditions,

 not to mention that the formed products can again be destroyed by new electron collisions.

#17.3.3
 For pure CO2 splitting,

 this is not much of an issue,

 since CO and O2 (together with small amounts of O3) are basically the only products that can be formed.

#17.3.4
 However,

 when combining CO2 with other reactants,

 such as CH4, H2O or H2, a wide variety of products can be formed,

 including syngas (CO and H2) and higher hydrocarbons (C2Hx,

 C3Hy,

 C4Hz) as well as several oxygenates,

 e.

g. methanol,

 ethanol,

 dimethyl ether,

 formaldehyde,

 acetaldehyde and carboxylic acids.

 For that reason,

 the combination with catalysis is also highly desirable for plasma technology when targeting the selective production of specific compounds (see Section 4.3).

#18
 4.1.3. Warm plasmas

Conventional thermal and non-thermal discharges #%cannot simultaneously provide a high level of non-equilibrium and a high electron density,

 whereas most prospective plasmachemical applications require both,

 i.

e. a high power (as translated in a high electron density) for efficient reactor productivity and a high degree of non-equilibrium to selectively populate certain degrees of freedom,

 such as vibrationally excited states (see Section 4.1.4 below).

86

#18.0.1
Recent studies have revealed that a transitional type of plasma,

 so-called warm discharge or warm plasma,

 which operates at the boundary – and hence shares properties – of both thermal and non-thermal plasmas,

 might be very promising for CO2 conversion.

#18.0.2
 These are non-equilibrium discharges,

 which are not only able to supply (re)active species,

 but also offer some controlled level of %%translational temperature[1].
[1] http://science.shinshu-u.ac.jp/~tiiyama/?page_id=4309

#18.0.3
 Although this translational gas temperature is still much lower than the electron temperature,

 it is significantly higher than room temperature and can easily reach up to 2000–3000 K.

 Hence,

 these warm plasmas are able to create the advantage of a non-equilibrium condition,

 while at the same time they can influence the chemical kinetics due to this higher gas temperature.

For the application of CO2 conversion,

 however,

 it is not the increased temperature that makes these discharges most interesting,

 but rather their characteristic %%electron energy distribution,

 which leads to most of the electron energy going into the vibrational excitation of CO2, as will be discussed below.

 The latter is indeed known to provide the most energy efficient and hence most important channel for CO2 dissociation.

#18.1
21,87 In fact,

 in recent modelling studies,

 it was suggested that the higher gas temperature inherent to these warm discharges is actually an unwanted effect.

88–90 As such,

 the development of ‘cooler’ warm discharges might be beneficial for further increasing the CO2 conversion and energy efficiency.

#19

#19.0.1
 4.1.4. CO2 dissociation channels

For a better understanding of the difference between non-thermal and %%warm discharges,

 and specifically between the different discharge types described in Section 4.2 below,

 we provide an overview of the different channels of energy transferred by electrons to CO2. As mentioned,

 the electrons receive their energy from the electric field in non-thermal plasmas,

 and subsequently,

 through collisions,

 this energy is distributed between elastic energy losses and different channels of excitation,

 ionization and dissociation.

 Fig.

 11 illustrates the fraction of the energy transferred to the different channels of the excitation,

 ionization and dissociation of CO2, as a function of the reduced electric field (E/n).

91

#19.0.2
The reduced electric field is the ratio of the electric field in the plasma over the neutral gas density and has distinctive values for different plasma types.

 For example,

 a dielectric barrier discharge (DBD),

 which is one of the most common types of non-thermal plasmas for CO2 conversion (see Section 4.2.1), has a reduced electric field in the range above 200 Td (Townsend; 1 Td = 10−21 V m2), whereas microwave (MW) and gliding arc (GA) discharges (which belong to the category of warm plasmas; see Sections 4.2.2 and 4.2.3) typically operate well below this range (about 50 Td).

Fig.

 11

#19.0.3

Fraction of electron energy transferred to different channels of excitation,

 as well as to the ionization and dissociation of CO2, as a function of the reduced electric field (E/n),

 as calculated from the corresponding cross-sections of the %[w:19.0.3-1]electron-impact reactions.

 The E/n regions characteristic for MW and GA plasma and for DBD plasma are indicated.

#19.0.4

 From Fig.

 11, it is clear that the value of the reduced electric field will have wide implications on the distribution of the electron energy among the different channels.

 In the region above 200 Td,

 70–80% of the electron energy goes into electronic excitation,

 about 5% is transferred to dissociation,

 5% is used for ionization (increasing with E/n),

 while only 10% goes into vibrational excitation (decreasing with E/n).

#19.0.5
 Around 50 Td,

 however,

 only 10% goes into electronic excitation and #%90% of the energy goes into vibrational excitations.

#19.0.6
 It is important to keep in mind that the addition of different gases (e.

g. Ar,

 He,

 N2, H2O, H2, CH4) has an influence on the distribution of these channels.

92

#19.1

Hence, even during the pure decomposition of CO2 into CO and O2, there will be an effect on this distribution.

The distribution of energy into different modes,

 and especially the fraction going into vibrational excitation,

 is very important,

 since,

 as mentioned above,

 it is known that the #%vibrational levels of CO2 can play an important role in the efficient dissociation of CO2. To achieve direct electron-impact dissociation,

 an electron #%needs to have enough energy (>7 eV) to excite CO2 into a dissociative (i.

e. repulsive) electronic state,

 which will lead to its dissociation into CO and O (see Fig.
12).

#19.1.1
As such,
 the amount of energy spent is much higher than the theoretical value necessary for C[double bond,

 length as m-dash]O bond breaking (5.5 eV).

 Due to the special nature of the CO2 molecule,

 a more efficient dissociation pathway is based on its vibrational excitation.

#19.1.2
 This pathway starts with electron-impact–vibrational-excitation of the lowest vibrational levels,

 followed by vibrational–vibrational (VV) collisions.

 This so-called ladder-climbing gradually populates the higher vibrational levels,

 which eventually leads to dissociation of the CO2 molecule (see also Fig.

 12). In this way,

 it is possible to dissociate CO2 more efficiently,

 since only the minimum amount of 5.5 eV for bond breaking is needed,

 compared to the overshoot in the case of electronic excitation–dissociation.

91

 Fig.

 12 Schematic of some CO2 electronic and vibrational levels,

 illustrating that much more energy is needed for direct electronic excitation–dissociation than for #%step-wise vibrational excitation,

 i.

e. the so-called %%ladder-climbing process (reproduced from ref.

 91 with permission from the Royal Society of Chemistry).

@@@
#20
 4.2. #%Different types of plasma set-ups used for CO2 conversion

As mentioned above,

 in recent years,

 there has been an increasing interest in the use of plasma technology for CO2 conversion.

 Experiments have been carried out in several types of plasmas.

 The most common types reported in the literature are dielectric barrier discharges (DBDs),

 microwave (MW) and gliding arc (GA) discharges,

 although other types have been used as well (e.

g. radiofrequency,

 corona,

 glow,

 spark and nanosecond pulse discharges).

 A DBD is a typical example of a ‘non-thermal plasma’,

 where the gas is more or less at room temperature,

 and the electrons are heated to temperatures of 2–3 eV (∼20 000–30 000 K) by the strong electric field in the plasma.

 The MW and GA discharges are examples of ‘warm plasmas’ (see Section 4.1.3 above).

 The gas can reach temperatures of up to 1000 K and more,

 and the electron temperature is typically up to a few eV.

 The operating conditions and characteristic features of the three major plasma types for CO2 conversion are explained here,

 as well as for some other plasma types that have also been applied for CO2 conversion.

4.2.1. Dielectric barrier discharge (DBD)

Dielectric barrier discharges (DBDs),

 also called ‘silent discharges’,

 have been known for more than a century.

 The first experimental investigations were reported by Siemens in 1857 and were concentrated on the most well-known industrial application of DBDs,

 i.

e. ozone generation.

80 For an extensive overview of the history,

 discharge physics and industrial applications of DBDs,

 we refer to the review of Kogelschatz et al.

80

A DBD consists of two plane-parallel or concentric metal electrodes and,

 as its name suggests,

 it contains at least one %dielectric barrier (e.

g. glass,

 quartz,

 ceramic material or polymers) in between the electrodes.

78,80,86,93 The purpose of the dielectric barrier is to restrict the electric current and thus to prevent the formation of sparks and/or arcs.

93

#20.1
A gas flow is applied between the (discharge) gap,

 which can typically vary from 0.1 mm (e.

g. in plasma displays),

 to over 1 mm (e.

g. for ozone generators) to several cm (e.

g. in %CO2 lasers).

78,86

#20.2
Some typical planar (top) and cylindrical (bottom) DBD configurations are shown in Fig.

 13. In general,

 DBDs operate at approximately atmospheric pressure (0.1–10 atm,

 but usually 1 atm),

 while an alternating voltage with an amplitude of 1–100 kV and a frequency of a few Hz to MHz is applied between both electrodes.

To ignite the discharge,

 or more specifically,

 to transport current in the discharge gap,

 an electric field high enough to cause breakdown in the gas needs to be applied.

 This breakdown voltage (Vb) can be determined according to Paschen's Law,

 and is a function of the pressure (p) and the gap distance (d):

 where C,

 D and γ are the gas (or mixture) specific parameters.

 Upon breakdown of the gas,

 most often a non-uniform plasma,

 consisting of a large number of micro-discharges (or filaments),

 is observed (indicated as purple in the top-left panel of Fig.

 13). This mode is called the ‘%filamentary mode’,

 and plasma formation is restricted to these micro-discharges.

 The occurrence of a filamentary mode,

 as opposed to a homogeneous mode,

 depends on the type of gas.

 Most gases,

 including CO2, give rise to a filamentary mode.

 It is stated that the volume of the micro-discharges,

 and hence the plasma volume,

 comprises about 1–10% of the total gas volume.

94,95 The rest of the gas is not ionized and serves as background reservoir to absorb the energy dissipated in the micro-discharges and to collect and transport the long-lived species created in the micro-discharges.

80 For a more detailed physical description on the formation of these micro-discharges,

 we refer to the review of Fridman et al.

86

]20200610_191426

#21
 4.2.2. Microwave (MW) discharge

Microwave discharges operate according to a different principle and belong to the group of warm plasmas.

 They are electrode-less and as their name suggests,

 the electric power is applied as microwaves,

 i.

e. electromagnetic radiation in the frequency range of 300 MHz to 10 GHz.

 There exist several different types of MW plasmas,

 e.

g. cavity induced plasmas,

 free expanding atmospheric plasma torches,

 electron cyclotron resonance plasmas and surface-wave discharges.

 For more details about the different microwave discharges,

 we refer to several reviews in the literature.

21,78,93,96

In the so-called %%surface-wave discharge,

 which is most commonly used for CO2 conversion research,

 the gas flows through a quartz tube – which is transparent to microwave radiation – intersecting with a rectangular wave guide,

 where the discharge is initiated,

 see Fig.

 14. This system,

 also called ‘guide-surfatron’,

 involves surface waves.

 The microwaves propagate along the interface between the quartz tube and the plasma column.

 The wave energy is absorbed by the plasma.

 Characteristic features are the wavelength (815 MHz or 2.45 GHz),

 which is comparable to the length of the apparatus,

 and the short period of the exciting microwave field.

 Surface-wave discharges can be created both at reduced and at atmospheric pressure,

 but in the pressure regime above 0.1 atm they approach a state of LTE.

78

#21.1
 4.2.3. Gliding arc (GA) discharge

A gliding arc (GA) discharge is also a warm plasma,

 combining advantages of both thermal and non-thermal plasma systems.

86 It is a transient type of arc discharge.

 At high currents,

 the periodic discharge typically evolves during one cycle from an arc to a strongly %%non-equilibrium discharge.

 The %%non-equilibrium GA is a very sophisticated physical phenomenon: this transitional quasi-equilibrium/non-equilibrium discharge is essentially non-uniform in time and in space,

 and includes an internal transition from thermal to non-thermal mechanisms of ionization.

86

A classical GA plasma is an %%auto-oscillating periodic discharge,

 where the gas flows between two diverging flat electrodes.

 When applying a potential difference between both electrodes,

 an arc plasma is formed at the narrowest gap,

 which is then dragged by the gas flow towards a rising interelectrode distance,

 until it extinguishes and a new arc is ignited at the shortest interelectrode gap.

#21.1.1
 More specifically,

 the length of the arc column increases together with the voltage until it exceeds its critical value (lcrit).

 At this point,

 heat losses from the plasma column begin to exceed the supplied energy and it is no longer possible to sustain the plasma in its %%LTE state,

 resulting in a fast transition into a non-LTE state.

#21.1.2
 The discharge cools rapidly to gas temperature but the plasma conductivity is maintained by a high value of the electron temperature (Te ∼ 1 eV,

 which is most suitable for efficient vibrational excitation of CO2). After this fast transition,

 the GA continues its evolution under non-LTE conditions,

 until the length reaches a new critical value (l ∼ 3·lcrit),

 leading to decay of the discharge,

 after which the evolution repeats from the initial breakdown.

#21.1.3

 During this cycle,

 up to 75–80% of the energy can be dissipated in the non-LTE zone of the gliding arc.

 It is this effect that permits the stimulation of chemical reactions in regimes quite different from conventional thermal reaction chemistry.

 When the GA is operated under milder conditions,

 i.

e. lower currents and high frequencies,

 this transition to the non-LTE phase can occur in the order of nanoseconds.

 As a result,

 the GA operates in the non-LTE regime starting almost immediately after its ignition,

 and a higher fraction of the discharge energy can be consumed by the non-LTE phase.

97–99

#21.1.4

The classical GA plasma,

 however,

 also exhibits some disadvantages.

 The flat 2D electrode geometry makes it less compatible with industrial systems,

 and also the gas conversion is non-uniform and quite limited,

 because a considerable fraction of the gas does not pass through the active plasma region.

 Moreover,

 a high gas flow rate is needed to drag the arc,

 so the gas residence time is limited,

 thereby further limiting the conversion.

 Therefore,

 a 3D cylindrical GA plasma reactor was developed a few years ago,

 which makes use of vortex flow stabilization.

#21.1.5
100 The gas flows in the reactor through a tangential inlet.

 An arc is again formed between both electrodes,

 and is dragged with the tangential gas flow,

 thereby expanding until it extinguishes,

 followed by a new cycle.

 Basically,

 the arc is again gliding between the anode and cathode,

 and it is stabilized in the centre of the reactor.

 Depending on the diameter of the anode tube,

 a forward or reverse vortex gas flow is created.

 If the anode diameter is equal to the cathode diameter,

 the gas can leave the reactor through the anode outlet,

 leading only to a forward vortex flow.

 On the other hand,

 if the anode diameter is smaller than the cathode diameter,

 the gas cannot immediately leave the reactor,

 and will first flow upwards close to the walls,

 in a forward vortex.

 As this gas is still cold,

 it creates an isolating and cooling effect,

 protecting the reactor walls from the warm plasma arc in the centre.

 When it reaches the upper end of the reactor,

 it will have lost some speed due to friction and inertia,

 and when flowing downwards,

 it moves in a smaller inner vortex,

 a so-called reverse vortex,

 where it mixes with the plasma arc,

 resulting in a more energy-efficient conversion.

 The reverse vortex flow GA is also called a ‘gliding arc plasmatron’ (GAP).

 Fig.

 15 shows the difference between these two types of GAs.

#22 ==> DROP
 4.2.4. Other plasma types used for CO2 conversion

Besides the above three main discharge types for CO2 conversion,

 some research is also being carried out with other plasma types,

 which are briefly discussed here.

 These include radio frequency (RF) discharges,

 several different atmospheric pressure glow discharges (APGD),

 corona discharges,

 spark discharges and nanosecond pulsed discharges.

RF discharges usually operate in the 1–100 MHz frequency range,

 resulting in a corresponding wavelength (300–3 m) much larger than the plasma reactor dimensions.

 The %%power coupling can be done through capacitive or inductive coupling,

 resulting in capacitively coupled plasma (CCP) and inductively coupled plasma (ICP).

 These kind of discharges are mainly applied to %%thin-film deposition,

 plasma etching,

 the sputtering of materials and as an ion source in mass spectrometry,

96 but some research is also being performed for CO2 conversion applications,

 as is illustrated in Section 5. An RF source operating at low pressure,

 both with and without the influence of an external magnetic field,

 has been used.

 The advantages for CO2 conversion are its capability to allow obtaining high electron densities at low gas temperature.

When a sufficiently large electric field is applied,

 %%corona discharges occur near sharp points,

 edges or thin wires when used as an electrode.

 When a high negative voltage is applied to the electrode,

 it acts as a cathode and is considered as a negative corona discharge.

 When a positive voltage is applied,

 it is considered as a positive corona discharge.

#22.1
 Corona discharges are always non-uniform,

 with a strong electric field,

 ionization and luminosity close to the wire/sharp electrode,

 whereas the charged particles are dragged to the other electrode by weak electric fields.

 They are often operated in a pulsed mode,

 mostly to increase the power,

 while inhibiting the transition of the streamer formation into sparks.

21 An advantage of corona discharges compared to DBDs is that they are relatively easy to establish; however,

 their performance in CO2 conversion processes is quite similar,

 as will become clear from Section 5.

When a streamer is able to connect two electrodes,

 without the presence of a pulsed power supply (see corona discharge above) or the presence of a dielectric (see DBD),

 a spark discharge can develop by further growth of the current.

21 However,

 when the amount of power provided is restricted,

 the discharge cannot develop into a stationary (thermal) arc and instead the discharge extinguishes within several hundred microseconds.

 Hence,

 spark discharges consist of an initiation of streamers that develop into highly energetic spark channels,

 which then extinguish and reignite periodically.

 Lightning is a typical example of a spark discharge.

#22.2
A wide variety of plasma set-ups fall under APGDs,

 such as miniaturized direct current (dc) GDs,

 microhollow cathode dc discharges and RF discharges as well as DBDs.

78 The main advantage of APGDs is the absence of vacuum conditions compared to with regular glow discharges,

 and also operating without elevated temperatures.

 Depending on the gas mixture and electrode configuration,

 the discharge can operate in a stable homogeneous glow or filamentary glow mode.

 For example,

 a DBD can operate in APGD mode,

 and in this case the discharge benefits from the average power densities of a DBD but operating in a uniform homogeneous glow mode,

 thus benefiting uniform gas treatment.

21 This discharge is interesting for DRM due to its special characteristics of electron density (3 × 1012 cm−3), electron temperature (∼2 eV,

 suitable for the vibrational excitation of CO2) and plasma gas temperature (900 K),

 which is lower than that of thermal plasma but higher than that of DBDs and corona discharges.

Finally,

 nanosecond pulsed discharges are basically discharges that rely on repetitively pulsed excitation,

 through a nanosecond scale pulse rise time and duration.

 This leads to a highly non-LTE state with very high plasma densities for a relatively low power consumption due to the short pulse durations.

 Whereas (sub)microsecond pulsed discharges are initiated by Townsend discharges,

 nanosecond pulsed discharges ignite instantaneously,

 i.

e. without the involvement of secondary electrons.

 Furthermore,

 the discharge remains in a glow-like (rather than filamentary) mode despite the high electric field.

 The interest in shorter pulses is not because of the duration of the discharge itself,

 but rather because they offer better control of the electron energy than continuous wave discharges,

 depending on the pulse length.

101 Thus,

 more energy can be directed towards the desired dissociation channels.

#23
 7. Conclusions and outlook

The conversion of CO2 – preferably into value-added products – is considered one of the great challenges of our century.

 In the past decade,

 substantial progress with several novel technologies has been made.

 The last section of this review intended to provide the reader with a state-of-the art and critical assessment of an – up till now – rather underexposed emerging technology: the plasmachemical conversion of CO2. To achieve this,

 we provided an introduction to the basic concepts of plasma,

 and we demonstrated its viability as a gas conversion technology,

 finally putting it in the broader context of its peers.

From the advances in the area of CO2 conversion discussed in this review,

 one outcome stands out without doubt.

 The question is not ‘if’ one of these novel technologies will be industrially competitive,

 but rather ‘when’ and ‘which one(s) will play the leading role’.

 To shine a brighter light on – the final burning question – whether plasma technology could be the answer – or at least be part of the equation – we briefly summarize here the arising opportunities and challenges for plasma technology in the field of CO2 conversion.

#23.1
Plasmas possess some important advantages over certain other (novel) technologies: (i) they can operate at room temperature using any source of (renewable) electricity,

 (ii) they have a large flexibility in terms of the feeds that need to be processed,

 (iii) they provide an extremely flexible ‘turnkey’ process,

 which allows for the efficient storage of energy,

 peak shaving and grid stabilization,

 (iv) the reactors have low investment and operating costs,

 (v) they have a simple scalability both in size and applicability,

 and (vi) last but not least,

 the technology does not rely on rare earth materials – making it rather unique at this point.

 This unprecedented combination of features gives plasmachemical conversion a very high overall flexibility,

 making it an extremely useful and valuable technology for CCU.

The flip side of the coin is that the reliance of plasma technology on indirect solar energy in the form of electricity is – at the same time – a limiting factor for the solar-to-fuel conversion efficiency,

 especially compared to technologies that can directly harvest solar energy.

#23.2
 Nonetheless,

 this also allows plasma technology to rely on other renewable energy sources,

 and more importantly,

 it adds to its overall – location and process – flexibility,

 since it is not dependent on the availability of sunlight.

 More urgent,

 however,

 is the issue of product separation.

 From all the data available in the literature,

 it is clear that converting CO2 – with or without an additional hydrogen source – always yields a mixture of products after reaction.

 This implies the need for an – often expensive – post-processing separation step.

#23.3
From the benchmarking discussion,

 it is clear that plasma technology can definitely play an important role in the field of CO2 conversion,

 and it is not beyond our grasp to think about its eventual commercial implementation,

 be it on a large or small scale.

 Nevertheless,

 as always,

 only a few candidates seem suitable for the specific task at hand,

 as we outline here.

#23.3.1
Two main CO2 conversion strategies were discussed: (i) pure CO2 splitting and (ii) CO2 conversion in combination with a co-reactant serving as the hydrogen source,

 i.

e. CH4, H2 and H2O, yielding processes named the dry reforming of methane (DRM),

 the hydrogenation of CO2 and artificial photosynthesis,

 respectively.

#23.3.2

 At this time,

 the conversion of CO2 through the latter two processes is – although possible – inefficient in a plasma-only set-up,

 not to mention industrially undesirable,

 due to the formation of possibly dangerous mixtures to be handled.

#23.3.3
 In the future,

 the combination of plasma with other technologies,

 such as catalysis or electrolysis,

 could solve these issues.

 On the contrary,

 for both pure CO2 splitting and DRM,

 the proposed energy efficiency target of 60% has already been surpassed by several types of plasma reactors,

 resulting in a solar-to-fuel conversion efficiency for the production of syngas above – the required – 20% mark.

#23.3.4
In the short run,

 pure CO2 splitting using the most energy-efficient set-ups,

 i.

e. MW and GA discharges,

 appears to have a high potential.

 In this case,

 pure CO and O2 could be produced,

 after a separation step,

 or a pure CO stream when in situ trapping of the O2 can be successfully implemented,

 e.

g. by combination with other technologies or through the addition of scavengers.

#23.3.5

In the long run,

 it seems evident that CO2 conversion in combination with a hydrogen containing co-reactant has the highest potential for the efficient production of value-added products,

 such as alcohols,

 aldehydes,

 esters and acids.

 In particular,

 the %%direct oxidative pathway[직접 산화 경로,

 in which the intermediate syngas step is circumvented,

 has great potential.

#23.3.6
 For now,

 however,

 a lot of research in this area is still needed to #%increase the selectivity towards these valuable bulk chemicals over the currently produced syngas.

 This will most probably need to be achieved in combination with catalysts.

 However,

 even today,

 APGD and GA discharges already provide an energy-efficient alternative to produce syngas in any desired ratio through DRM.

#23.3.7

By all means,

 plasma technology is not just an overlooked unicorn – although its combination of features does make it quite unique for CCU – but,

 as mentioned several times throughout this work,

 and just like for all other emerging technologies in this field,

 several important challenges remain.

#23.4
 General challenges comprise the need for further fundamental research,

 concerning: (i) the plasmachemical processes taking place in warm discharges,

 such as MW and GA,

 which stimulate vibrational excitation; whereby the latter,

 representing the most energy-efficient dissociation pathway,

 should be further exploited by enhancing the non-equilibrium character of these plasmas to further improve the energy efficiency,

 (ii) the combination of plasma with catalysis and the possibility of taking advantage of the synergetic effects and the selective production of value-added compounds,

 (iii) in situ O/O2 trapping by using scavengers,

 or combinations with other technologies,

 such as catalysis or %%SOEC,

 to further enhance the conversions and yields towards the desired value-added compounds,

#23.4.1
 (iv) the demonstration of successful scale-up for other discharges than DBDs and (v) the production and tuning of efficient power supplies for generating and sustaining the plasma.

#23.5
Moreover,

 some important discharge-specific research challenges can also be identified.

 For MW plasmas,

 the ultimate goal should be to achieve the same energy efficiency at atmospheric pressure as currently obtained at reduced pressure for CO2 splitting,

 while more research towards DRM is essential.

 For GA plasmas,

 the limited amount of gas that passes through the active arc region,

 and thus that can be converted by the plasma,

 is currently limiting the overall CO2 conversion,

 and more research in this direction is needed,

 e.

g. by improving the reactor design.

 Furthermore,

 some other plasma reactors show good performance,

 but the available data and insights are still limited,

 thus requiring more research to explore their full potential.

 Of course,

 inherent to every review,

 the above analysis represents the current state-of-the-art.

 Plasma-technology-based CO2 conversion is relatively new and it is clearly a fast advancing field with – just like for any emerging technology – ample room for improvement and new (interdisciplinary) developments.

It appears that the ultimate plasma for CO2 conversion would be a system with a high electron density (Ne) and a low electron temperature (Te) – resulting from a low reduced electric field (E/n) – which are essential to stimulate and achieve a high fraction of vibrational excitation.

 At the same time,

 this system should operate at a low gas temperature (Tg) to minimize the VT relaxation losses and backward recombination reactions.

#23.6
 Finally,

 to be industrially attractive,

 this should be achieved at atmospheric pressure.

Future research towards the #%direct oxidative production of oxygenates,

 as well as multi-reforming processes with a combination of gases (e.

g. CO2, CH4 and H2O or O2) or several reforming processes in series,

 using plasma technology appears very promising and should be pursued.

 Furthermore,

 more interdisciplinary research into the combination of plasmas with other novel technologies is highly desirable.

 For catalysis,

 the combination is already proving alluring,

 and it is our opinion that combinations with electrolysis,

 although even more challenging,

 could also lead to synergetic effects.

 As is the case for many important issues brought forward in the current age,

 with a high probability the future will rely on a true amalgam of technologies and solutions,

 each for its specific tasks,

 rather than the ‘one solution (or technology) fits all’ mentality of the old age.

#23.7

From the current analysis,

 it is evident that pure CO2 splitting could reach industrial implementation at a faster pace.

 Nevertheless,

 CO2 conversion using a hydrogen source as a co-reactant should certainly be further pursued,

 since – when successful – in the long run it offers us the possibility of producing a wide variety of value-added chemicals and fuels,

 starting from the same building block and allowing the flexibility to tune the output depending on the market's needs.

 On that account,

 we believe plasmas could be – at least part of – the bright light that shines on our horizon.

Acknowledgements

We would like to thank W.

 Wang (University of Antwerp) for providing the data on the thermal equilibrium conversions.

 Furthermore,

 we acknowledge financial support from the IAP/7 (Inter-university Attraction Pole) programme ‘PSI-Physical Chemistry of Plasma-Surface Interactions’ by the Belgian Federal Office for Science Policy (BELSPO),

 the Methusalem financing of the University of Antwerp,

 the Fund for Scientific Research Flanders (FWO; Grant no.

 G.

0383.16N, G.

0254.14N and G.

0217.14N),

 the TOP research project of the Research Fund of the University of Antwerp (grant ID.

 32249).

#24
 4.3. Plasma-catalysis

As with most of the technologies described in Section 3, plasma set-ups can also be combined with a packing material or catalyst,

 giving rise to plasma-catalysis.

 Plasma-catalysis is an emerging branch of plasma processing at the interface of a variety of disciplines,

 including physical chemistry,

 material science,

 nanotechnology,

 catalysis,

 plasma physics and plasma chemistry.

 In short,

 its objective is to enhance plasma reactions by adding a catalyst to the reaction cycle and vice versa.

#24.1
 Theoretically speaking,

 combining plasma with catalysis offers the best of both worlds.

 Inert molecules are activated by the plasma under mild conditions,

 and subsequently the activated species selectively recombine at the catalyst surface to yield the desired products.

 This will be especially important to further advance and optimize the %%direct oxidative liquefaction pathway of plasmachemical CO2 conversion,

 in order to selectively produce the desired liquid products.

#24.2
 In this section,

 we present a brief overview of the different approaches and possible interactions between the plasma and the catalyst.

 For more extensive details,

 we refer to several broad reviews on this specific topic that have recently been published.

83,102–104
4.3.1. Approaches

Plasmas and catalysts can be combined in two main configurations,

 as illustrated in Fig.

 16. In the first,

 the so-called two-stage configuration (Fig.

 16(b)),

 the catalyst is spatially separated from the plasma region,

 either upstream or downstream,

 but the main configuration is downstream.

 In the second,

 the so-called one-stage configuration (Fig.

 16(c)),

 the catalyst is placed inside the discharge region.

 In a traditional thermal catalysis experiment,

 molecules are dissociatively adsorbed onto the catalyst with the energy being supplied in the form of heat.

 In plasma-assisted catalysis,

 species are activated by the plasma due to excitation,

 ionization or dissociation by electrons in the gas phase or on the catalyst surface.

 The major difference between the one-stage and two-stage configuration is the kind of species to which the catalyst is exposed.

 In the two-stage configuration,

 the end-products and the long-lived intermediates will interact with the catalyst,

 while in the one-stage configuration,

 the catalyst can also interact with all the short-lived species,

 including excited species,

 radicals,

 photons and electrons.

 Furthermore,

 in this configuration the catalyst may also be influenced by the plasma and vice versa (see below).

#24.3
 Besides plasma-catalysis,

 the #%preparation and modification of catalysts by plasma treatment is gaining increased attention,

 especially for catalysts with a low thermal stability.

103

The most widely investigated and,

 for this review,

 most interesting configuration is the one-stage configuration,

 in which the catalyst is placed inside the discharge region,

 either completely or only partially occupying the discharge zone.

 The catalyst itself can be introduced in the discharge as pellets,

 (fine) powders,

 foams,

 %%honeycomb monoliths,

 different electrode materials and electrode coatings or as coated %%quartz wool.

 The ease of adding a catalyst into the discharge zone greatly varies depending on the type of plasma reactor used.

#24.4
 In general,

 due to their simple geometry and operation close to room temperature,

 implementation of a catalyst in a DBD reactor is very easy.

 Although MWs also have a simple geometry,

 due to the high gas temperature inside the discharge zone (1000–2000 K compared to 300–400 K for DBD) catalysts are often placed downstream,

 due to their low thermal stability.

 Finally,

 GA discharges have rather complex geometries and the same higher gas temperatures,

 thus catalysts are typically introduced downstream,

 although the use of a %%spouted bed has also been reported.

105 If these MW and GA discharges can be operated at slightly lower temperatures (≤1000 K),

 this would yield new possibilities.

 It would also open up the way for using sufficiently thermally stable catalysts inside the discharge zone,

 and at the same time it would allow thermal activation of catalysts inside the discharge zone by the plasma.

#24.5
4.3.2. Synergetic effects

The resulting interactions when combining a plasma with a catalyst for plasma-based CO2 conversion often yield improved process results in terms of conversion,

 selectivity,

 yield and energy efficiency.

 This surplus effect,

 as shown in Fig.

 17, is a complex phenomenon originating from the interplay between the various plasma–catalyst interactions and is often termed ‘synergy’,

 when the combined effect is larger than the sum of the two separate effects.

102 Note that most research to date regarding this effect #%has been performed for DBDs.

 The complex interactions can be subdivided into two categories: the effects of the plasma on the catalyst,

 and vice versa,

 the effects of the catalyst on the plasma.

102,107 Second,

 it is important to distinguish between the two types of effects: physical and chemical effects.

 While the physical effects are mainly responsible for gaining a better energy efficiency,

 the chemical effects can lead to an improved selectivity towards the targeted products.

 In the case of CO2 splitting,

 mainly CO and O2 are formed,

 so the primary added value of the catalyst is to increase the energy efficiency,

 although the conversion can also be improved by chemical effects,

 such as enhanced dissociative chemisorption due to the catalyst acid/basic sites.

 When adding a co-reactant (e.

g. CH4, H2O, H2), the catalyst allows modifying the selectivity towards the targeted products.

#24.6

An overview of the plasma–catalyst interactions is given in Fig.

 18. When adding a catalyst,

 the following effects on the plasma have been reported: (i) an enhancement of the electric field through the geometric distortion and surface roughness; (ii) the formation of micro-discharges inside the pores of the catalyst material,

 due to the very strong electric field inside the pores,

 leading to different characteristics compared to the bulk; (iii) a change in the discharge type,

 because the presence of insulating surfaces promotes the development of surface discharges; (iv) the adsorption of species on the catalyst surface,

 which affects their concentration and conversion due to longer retention times.

 All the effects of the catalyst on the plasma can thus generally be considered as physical effects.

 The reported effects of the plasma on the catalyst,

 on the other hand,

 are of both a physical and chemical nature.

 They include: (i) changes in its physico-chemical properties,

 such as a higher adsorption probability at the catalyst surface,

 a higher catalyst surface area,

 a changed catalyst oxidation state,

 the reduction of metal oxide catalysts to their metallic form,

 reduced coke formation on the surface and a change in the catalyst work function; (ii) the formation of hot spots on the surface due to the formation of strong micro-discharges; (iii) catalyst activation by photon irradiation emitted by the excited plasma species (although this effect is probably of only minor importance due to the low photon fluxes); (iv) lowered activation barriers due to there being more reactive vibrationally excited plasma species and consequently a greater possibility for non-adiabatic barrier crossings; (v) changes in the reaction pathways due to the presence of a wide variety of (re)active species.

#24.7
While the physical effects have been more extensively studied,

 such as the plasma behaviour in packed-bed DBD reactors108 or inside catalyst pores,

109 the chemical effects are less understood,

 mainly because they are often correlated with the physical effects.

 Indeed,

 in a DBD,

 the catalyst is mostly introduced as a packed bed,

 making it difficult to distinguish between the two effects.

 Hence,

 more systematic studies on both the physical and chemical effects of the catalyst material are highly needed.

102 Furthermore,

 as summarized in Fig.

 19, the plasma and catalyst both have an influence on the gas composition,

 and at the same time the plasma influences the catalyst properties and vice versa,

 as mentioned above.

 Therefore,

 both the gas composition and the plasma and catalyst properties continuously influence each other,

 and at the same time are influenced by the plasma chemistry and surface chemistry.

 Thus,

 it is recommended to develop tailored catalysts for plasma-catalysis,

 rather than simply relying on classical catalysts.

 This is discussed further in Section 5.

Finally,

 it is worth mentioning that besides CO2 conversion,

 the combination of plasma with catalysts is also promising for nanomaterial synthesis,

 such as for the growth of carbon nanotubes,

 nanofibres,

 and graphene.

 To date,

 research on this topic has been mainly focused on pure methane plasmas,

 instead of CO2 plasmas.

 This is,

 however,

 outside the scope of the present review,

 but we refer to another recent review paper,

 where these applications are discussed in detail.

102

]XXX

------------------------------------------ [resource] 20200526_153656
#%Plasma-Driven Catalysis	keyword	青２
%%flexibility to be scaled up and down	notice	緑４
#2	location number	青２ / オレンジ色１

1	([^\d])(\.|\,)	$1$2\n\n
	([^\d]{2,}?)(\.|\,)	$1$2\n\n

/ ------------------------------------------ [resource] 20200526_153656 /

1	write “aaa” || select / M – w > a (duplicate) / C – f > “@x3” > Ret x 2 / select ==> “@x3” || cut [M – x] || M – Tab (back to the orig) / M – v (paste) || M – Tab (to the dup) / select ==> loc label || M – c || C – w (close the dup) / M – v (paste) / new label ==> edit / C – s (save)