https://pubs.rsc.org/en/content/articlelanding/2017/cs/c6cs00066e#!divAbstract

M-47

=========================[ 20200601_123641
#1
 Plasma technology – a novel solution for CO2 conversion?

Abstract

CO2 conversion into value-added chemicals and fuels is considered as one of the great challenges of the 21st century.

 Due to the limitations of the traditional thermal approaches,

 several novel technologies are being developed.

 One promising approach in this field,

 which has received little attention to date,

 is plasma technology.

 Its advantages include mild operating conditions,

 easy upscaling,

 and gas activation by energetic electrons instead of heat.

 This allows thermodynamically difficult reactions,

 such as CO2 splitting and the dry reformation of methane,

 to occur with reasonable energy cost.

 In this review,

 after exploring the traditional thermal approaches,

 we have provided a brief overview of the fierce competition between various novel approaches in a quest to find the most effective and efficient CO2 conversion technology.

 This is needed to critically assess whether plasma technology can be successful in an already crowded arena.

 The following questions need to be answered in this regard: are there key advantages to using plasma technology over other novel approaches,

 and if so,

 what is the flip side to the use of this technology? Can plasma technology be successful on its own,

 or can synergies be achieved by combining it with other technologies? To answer these specific questions and to evaluate the potentials and limitations of plasma technology in general,

 this review presents the current state-of-the-art and a critical assessment of plasma-based CO2 conversion,

 as well as the future challenges for its practical implementation.

#2

1. Introduction
Environmental and energy applications of low temperature plasmas are gaining increasing interest worldwide.

 The central research question is whether plasma-based solutions can yield a valuable alternative to existing thermal processes and whether they can compete with other novel gas conversion technologies.

 Nowadays,

 the conversion of CO2 into chemicals and fuels is a hot topic.

 The worldwide transition to renewable energy gives plasma processes a clean electricity source,

 and due to their high operation flexibility,

 plasmas are very suitable for storing this intermittent renewable energy in a chemical form,

 i.

e.

 as fuels and chemicals.

1.1. CO2 mitigation and valorisation
Throughout history,

 the use of natural resources has played a major role in the rapid development of the human race.

 Among these resources,

 fossil fuels in particular have contributed to a fast and unprecedented development in human society.

 Still,

 this comes with a great cost,

 since burning fossil fuels leads to the emission of large amounts of the greenhouse gas CO2. Because these anthropogenic CO2 emissions outpace the natural carbon cycle,

 atmospheric CO2 concentrations have been increasing from 280 ppm since the beginning of the industrial revolution to 400 ppm in 2014.1 With high certainty,

 it can be said that it is this increase that has led to the current adverse global environmental climate changes,

1 which have a growing detrimental effect on our climate and environment,

 and that represent a severe threat to our current society and future generations in general.

2–5

Therefore,

 the conversion of this main greenhouse gas into value-added chemicals and liquid fuels is considered as one of the main challenges for the 21st century.

1,2 The aim is not only to tackle climate change,

 but also to provide an answer to our dependence on fossil fuels.

 As stated by Goeppert et al.

,6 “Whether humankind uses up most of the fossil fuel resources (combined with carbon capture) or uses increasingly alternative energies,

 the need for transportation fuels and materials that we currently obtain from petroleum and natural gas will remain.

 With increasing population,

 products based on carbon from plastics to medicines will also be required in increasing quantities.

 In order to fulfil the demand for carbon-based products,

 CO2will have to be recycled in an anthropogenic version of nature's own carbon cycle.

 Carbon capture and recycling (CCR) will capture CO2from any source,

 and eventually mainly from the atmosphere,

 and recycle it to new materials and fuels using any alternative energy source.

”

Utilization of this waste and converting it into a new feedstock not only complies with the framework of sustainable and green chemistry7,8 but also fits within the ‘cradle-to-cradle’ concept.

9 By generating useful products out of CO2 we create the possibility to effectively close the carbon loop.

 This has already resulted in a booming interest in technologies that can convert CO2 into value-added products,

10–12 since they can effectively convert waste into new feedstocks following the cradle-to-cradle principle.

9 Besides chemical conversion,

 which is the principle focus of this review,

 CO2 also has other applications in the field of carbon dioxide capture,

 storage and utilization,

 such as its fixation and technological utilization,

 for these and other processes,

 as well as in carbon capture,

 for which we refer to several existing reviews in the literature.

12–19

Besides the traditional thermal CO2 conversion,

 several alternative technologies are being investigated,

 such as electrochemical,

 solar thermochemical,

 photochemical and biochemical pathways,

 either with or without catalysts,

 as well as all their possible combinations.

 Their advantages and disadvantages are briefly discussed herein,

 as they form the context for a novel approach considered to have great potential in recent years,

 which is the approach based on (non-thermal) plasma.

20,21 Several options are being investigated in this regard,

 including both pure CO2 splitting into CO and O2, as well as the reaction with other gases,

 like CH4 (dry reforming of methane),

 H2 (hydrogenation of CO2) or H2O (artificial photosynthesis),

 aiming for the production of syngas and valuable oxygenates,

 such as methanol,

 formaldehyde and formic acid.

#3
1.2. Solar fuels
The important difference between the traditional thermal conversion approaches and the emerging technologies is their independence of burning fossil fuels to provide the necessary thermal heat to drive reactions.

 More precisely,

 biochemical pathways rely on the natural photosynthesis process to convert light (either natural or artificial) into biomass,

 which can then be harvested and further processed.

 Other emerging technologies,

 such as the solar thermochemical and photochemical processes rely on direct solar energy.

 The average solar flux striking the earth's surface is 175 W m−2, which represents more energy striking the earth's surface in two hours,

 i.

e.

 640 EJ,

 than the worldwide energy consumption from all sources combined in 2008, i.

e.

 514 EJ.

22 The solar thermochemical process makes use of concentrated solar heat,

 while the photochemical process relies on the energy of photons.

 Ultimately though,

 the electrochemical and plasmachemical processes rely on electricity.

 Fig.

 1 gives an overview of the different novel technologies and their principal use of renewable energy for the conversion of CO2 in a carbon neutral cycle.

The reliance of electrochemical and plasmachemical conversions on electricity at first seems to limit their use as a greenhouse gas mitigation technology,

 since currently,

 producing electricity generally results in CO2 emissions.

 This idea though could not be further from the truth due to the worldwide transition to renewable energy sources,

 such as solar and wind energy.

 In 2014, the estimated renewable energy share of the global final energy consumption was already 19.2%,

 while by the end of 2015, the estimated renewable energy share of global electricity production was 23.7%.

23 It is even at such a stage that the large-scale adoption of these renewable energy sources poses a challenge for the efficient storage and easy transport of the electricity produced,

 i.

e.

 not only regarding the need for peak shaving,

 but more importantly the need for technologies to follow the irregular and at times intermittent supply of renewable electricity in a flexible way.

 While storage in batteries is possible,

 it is less efficient than chemical storage in fuels.

24 Such fuels,

 often referred to as carbon neutral fuels or solar fuels,

 offer a much higher gravimetric and volumetric energy storage capacity,

 have much higher energy densities than electrical storage techniques and they match the existing worldwide liquid fuel infrastructure.

12,24

In the first instance,

 the reactions in which CO2 is involved can be divided into two categories: the production of chemicals and the production of fuels.

 The latter is considered as the most suitable target for the conversion of large volumes of CO2 since its market size is 12–14 times larger than the former.

 One of the most interesting compounds is methanol,

 which is positioned exactly in the middle of these two categories,

 being at the same time a raw chemical and a fuel,

 used in both combustion engines and fuel cells.

25

To achieve the transformation of CO2 into value-added chemicals or fuels,

 the reactions that are of greatest interest involve the conversion of CO2 with a %%co-reactant that acts as a hydrogen source (like CH4, H2 or H2O).

 Due to the existing infrastructure,

 liquid products are preferable to gases,

 for most applications at least.

 Two approaches can be considered to achieve this: the indirect oxidative pathway and the direct oxidative pathway.

 The main product of the former is syngas,

 a mixture of H2 and CO,

 which can be converted to almost any commercial bulk chemical or fuel in a second – albeit very energy intensively – step through methanol and/or Fischer–Tropsch synthesis.

10 In this case,

 it is of great importance to have a high degree of control over the H2/CO ratio to be able to steer the synthesis towards the desired products.

26 The %%direct oxidative pathway,

 on the other hand,

 tries to eliminate the energy-intensive middle man by converting the reactants immediately into hydrocarbons,

 short-chain olefins (e.

g.

 ethylene and propylene) and oxygenated products (e.

g.

 methanol,

 formaldehyde,

 dimethyl ether and formic acid).

Liquid products are more attractive over gaseous hydrogen,

 since – while in theory a ‘Hydrogen Economy’27 would be very attractive – the latter has a number of serious drawbacks due to its physico-chemical properties.

28 Furthermore,

 the infrastructure needed to safely transport,

 store and dispense hydrogen would be very expensive to roll out,

 while liquid chemicals match the already existing worldwide fuel infrastructure.

12,24 Hence,

 especially in the transportation sector,

 a transition from liquid–fossil-fuel-derived products (e.

g.

 gasoline,

 diesel fuel,

 kerosene) to a renewable and sustainable liquid fuel is highly desirable.

 Again,

 methanol is one of the most interesting possible candidates to fulfil these requirements.

 It is the simplest liquid chemical containing only one carbon.

 Although to date it is almost exclusively produced from natural gas (and shale gas) for economic reasons,

 it can easily be obtained from several (future) carbon sources,

 incl.

 CO2, biomass,

 biogas and landfill gas.

 Therefore,

 it has been proposed as a key solar fuel for the above-mentioned anthropogenic carbon cycle under the framework of a ‘Methanol Economy’.

6

To be economically competitive with the existing structures,

 the efficient production of these solar fuels is critical during the quest to find an effective CO2 conversion technology with the potential to be commercialized on a large scale.

#5
 2. Traditional thermal CO2 conversion approaches

We first briefly discuss the existing traditional (mainly thermocatalytic) approaches used on an industrial scale.

 As such,

 this section will act as a comparison for the novel technologies under development.

 This section is subdivided into: (1) pure CO2 splitting and (2) CO2 conversion in combination with a co-reactant,

 i.

e.

 CH4, H2 or H2O.

2.1. Pure CO2 splitting

Thermal CO2 splitting has not been very effective to date.

 This is not surprising from a thermodynamic point of view; the carbon–oxygen bonds are relatively strong (783 kJ mol−1)29 and the Gibbs free energy of formation (ΔG° = −394 kJ mol−1)24 clearly shows that CO2 is a highly stable molecule,

 requiring a substantial energy input,

 optimized reaction conditions and active catalysts for any chemical conversion to take place.

 Neither the entropy (TΔS°) nor the enthalpy (ΔH°) term seem favourable for its conversion.

2 The overall reaction is written as: CO2(g) → CO(g) + 1/2O2(g) ΔH° = +283 kJ mol−1 (R1) Of course,

 the high value of ΔH° does not mean that its conversion is not feasible.

 Indeed,

 strongly %%endothermic chemical reactions can be found in a large number of industrial processes used worldwide,

 a classic example being the steam reforming of methane (SMR):24,31 CH4(g) + H2O(g) → CO(g) + 3H2(g) ΔH° = +206 kJ mol−1 (R2) This highly endothermic reaction has found worldwide use.

 In the fertilizer industry,

 the H2 is used for the production of ammonia,

 while in the gas industry,

 this reaction is responsible for 95% of the worldwide H2 production.

 This shows that there is no reason to dismiss CO2 splitting just because it is highly endothermic.

 Hence,

 a fair amount of research towards this reaction has already been conducted,

 of which an overview can be found in the work of Rayne.

29

It is,

 however,

 clear that,

 without actively removing one of the products (i.

e.

 CO or O2),

 the equilibrium of this reaction lies strongly to the left.

 Thus,

 thermal CO2 splitting is thermodynamically and energetically only favourable at very high temperatures,

 as can be seen in Fig.

 2. At 2000 K for instance,

 the reaction is not very efficient: we can easily estimate that ca.

 92 kJ mol−1 would be needed to heat 1 mole of CO2 from 300 to 2000 K.

 Furthermore,

 the reaction enthalpy is equal to 245 kJ mol−1 at 2000 K.

 Based on a conversion of 1.5% at this temperature,

 the energy cost for the total conversion is ∼7.9 MJ mol−1, yielding an energy efficiency of only 4.4% with respect to the reaction enthalpy of 283 kJ mol−1 at 300 K.

 On the other hand,

 ca.

 184 kJ mol−1 would be needed to heat 1 mole of CO2 to 3500 K,

 and at this temperature the reaction enthalpy is equal to 206 kJ mol−1. Hence,

 based on a conversion of 80% at this temperature,

 the energy cost of the total conversion is then only ∼602 kJ mol−1, yielding an energy efficiency of 47% with respect to the reaction enthalpy of 283 kJ mol−1 at 300 K.

 While the conversion continuing to increase,

 above 3500 K the energy efficiency starts to decrease.

 At 5000 K,

 the conversion is 100% but the energy efficiency is only 35%,

 as can be deduced from Fig.

 2.

 Thus,

 it is clear that the equilibrium production of CO and O2 varies from less than 1% at temperatures below 2000 K up to 45–80% at the temperature range 3000–3500 K.

29,30 Therefore,

 the most pertinent studies regarding thermal CO2 splitting involve membrane reactor systems.

 Nigara and Cales32 used a calcia-stabilized zirconia membrane and CO as the sweep gas.

 At a temperature of 1954 K,

 they were able to reach a conversion of 21.5%,

 whereas the equilibrium production was a mere 1.2% at the same temperature.

32 The overall conversion,

 however,

 was much lower due to the permeation of O2 through the membrane,

 whereby it recombined with the CO sweep gas to form CO2. Itoh et al.

33 employed an oxygen permeable yttria-stabilized zirconia membrane and used argon as the sweep gas.

 Unfortunately,

 despite the removal of oxygen through the membrane,

 conversions of only up to 0.5% were obtained for a maximum temperature of 1782 K.

 Fan et al.

34 used a solid oxide (SrCo0.5FeO3) membrane reactor and methane as the sweep gas.

 Conversions of up to 10% were found at a temperature of 1213 K,

 which are one to two orders of magnitude higher than what could be expected to be attained conventionally.

 Nonetheless,

 the feed gas was diluted with four parts of helium per one part of CO2, and when this is taken into account,

 an effective conversion of only 2% was actually reached.

To summarize,

 these studies have demonstrated the possibility of producing CO and O2 by the direct thermal splitting of CO2 – at lower temperatures than the equilibrium predictions – by means of the use of semipermeable membranes to extract oxygen.

 Nevertheless,

 the attained overall effective conversions of 0.5–2% are too low to be considered practical for successful application on an industrial scale.

Because to date none of the above-mentioned alternative approaches to split CO2 at lower temperatures have yet realized acceptable conversions and energy efficiencies,

 thermocatalytic CO2 splitting is currently not applied on an industrial scale.

 The reason for this is the high energy consumption and,

 in addition,

 the lack of effective techniques for separating CO and O2 at high temperatures to avoid ending up with an explosive mixture.

 Nevertheless,

 we presented this brief summary of the initial efforts regarding thermal CO2 splitting to support a complete understanding of the matter,

 and because this work has laid the foundations for one of the novel technologies,

 i.

e.

 solar thermochemical CO2 splitting,

 discussed later (see Section 3.2).

2.2. Conversion of CO2 with a co-reactant

Due to the inherent high energy consumption and derived low energy efficiency of thermocatalytic CO2 splitting,

 the only practical way to reform CO2 consists of using a co-reactant.

 Thermodynamically speaking,

 it is significantly easier to convert CO2 when it is paired with a co-reactant that has a higher,

 i.

e.

 less negative,

 Gibbs free energy.

24 Some suitable candidates are CH4 (ΔG° = −50.7 kJ mol−1) and H2 (ΔG° = 0 kJ mol−1).

 In essence,

 these hydrogen-bearing energy carriers give up their intrinsic chemical energy to promote the conversion of CO2.

As such,

 it is no surprise that the most widely investigated traditional processes to convert CO2 involve the reaction with either CH4 or H2. The former is one of the best known traditional processes for reforming CO2 into synthesis gas or syngas,

 which is a mixture of H2 and CO.

 The reaction with H2 is known as the Sabatier reaction,

 which is a well-known process to generate CH4 (and H2O).

 Additionally,

 the combination of CO2 and H2 can also be used to produce methanol through the methanol synthesis process.

 A final process of interest to mention is the combined conversion of CO2 and H2O,

 a technique for which there is no real traditional approach.

 Nevertheless,

 we briefly mention it here because water is an interesting co-reactant to pursue for the growing array of novel techniques.

 After all,

 H2O is not only the most ubiquitous and cheapest hydrogen source,

 compared to CH4 and H2, but converting CO2 in combination with H2O to produce value-added products using renewable energy would successfully mimic natural photosynthesis.

35,36 It is interesting to note that besides CH4, H2 and H2O,

 other possible hydrogen sources could also be considered,

 such as %%glycerol.

 The use of glycerol as a hydrogen donor has already been suggested and successfully implemented for different technologies,

 such as its use as a hydrogen donor (and green solvent) in catalytic transfer hydrogenation–dehydrogenation reactions of various unsaturated organic compounds;37 its use as a hydrogen donor for the production of CH3OH from CO2 in a hybrid enzymatic/photocatalytic approach38 and its use in the plasma-based reforming of glycerol towards syngas,

39 which also led to the suggestion of using glycerol as a hydrogen donor for the possible in situ trapping of oxygen during the plasmachemical splitting of CO2.40 However,

 in this review,

 the focus lies on the above-mentioned three most commonly used hydrogen sources CH4, H2 and H2O.

#6
 2.2.1. CO2 + CH4: dry reforming of methane

The combined conversion of CO2 and CH4, known as the dry reforming of methane (DRM),

 is named analogous to its sibling conversion,

 namely the steam reforming of methane (SMR; reaction (2) above) – indicating the replacement of water by carbon dioxide: CH4(g) + CO2(g) → 2CO(g) + 2H2(g) ΔH° = +247 kJ mol−1 (R3) This process is,

 however,

 not as straightforward as the steam reforming of methane,

 because CO2 is a highly oxidized,

 thermodynamically stable molecule,

 while its reaction partner,

 CH4, is chemically inert.

 Hence,

 the process needs to be carried out at high temperatures (900–1200 K) in the presence of a catalyst,

 typically containing Ni,

 Co,

 precious metals or Mo2C as the active phase.

41,42Fig.

 3 illustrates the theoretical thermal conversion and energy efficiency as a function of temperature.

 At 1500 K,

 complete conversion is achieved,

 with an energy efficiency of 60%.

 However,

 the maximum energy efficiency of 70% is obtained before this at 1000 K,

 reaching a conversion of maximum of 83%,

 but this then decreases with increasing the temperature.

 Fig.

 3 Calculated theoretical thermal conversion (left axis) and corresponding energy efficiency (right axis) as a function of temperature for the dry reforming of methane.

 The dry reforming of methane (DRM) has quite a history.

 It was first studied by Fischer and Tropsch in 1928,42 and has been a challenge for chemical engineering ever since.

41 Since that time,

 the rationale for investigating this process has adapted itself several times to the spirit of the age.

 In its origin,

 it arose from a desire for alternative ways to produce fuels and chemicals (in combination with the Fischer–Tropsch synthesis) due to the limited supply of fossil fuels during the Second World War.

43 A renewed interest was found in the 1970s in the aftermath of the oil crisis,

43 again to circumvent the need for fossil fuels and with the idea of utilizing cheaper and more abundant natural gas.

 With the beginning of a new millennium and the increasing concern regarding climate change,

 DRM was seen as a way to convert the major greenhouse gas CO2 into useful products with the aid of natural gas.

31,44 To date,

 a true amalgam of environmental and economical motivations exist,

 such as the conversion of the greenhouse gas CO2, the capability of using biogas as a feedstock,

 the search for a convenient way to liquefy CH4 for easier transport,

 and the availability of cheap CH4 through shale gas.

12,18,31,41,42,44–46

Alas,

 despite all the bright outlooks,

 there is one major pitfall,

 namely the process’ inherent susceptibility for soot deposition and the detrimental effect this has on the process through deactivation of the catalyst.

 Due to this drawback,

 DRM is to date not yet (widely) used on an industrial scale.

 Of course,

 a lot of research is still ongoing towards modified catalysts to circumvent this coking issue,

 which was originally also a big problem for the currently widely adopted steam reforming of methane.

 Nevertheless,

 the inability to transform the alluring promises of DRM into reality through the traditional thermal methods – among other reasons– has sparked and fuelled the growing interest for alternative reforming technologies,

 as is discussed in Sections 3 and 4.

#7
 2.2.2. CO2 + H2: hydrogenation of CO2

Both the complete hydrogenation of CO2 to CH4, known as the Sabatier reaction or the methanation of CO2, and the selective hydrogenation of CO2 to methanol are well-known commercially interesting processes.

47 The #%catalytic hydrogenation of CO2 to methane is a thermodynamically very favourable process:48 CO2(g) + 4H2(g) → CH4(g) + 2H2O(g) ΔH° = −165.3 kJ mol−1 (R4) However,

 due to the high oxidation of the carbon,

 its reduction consists of an eight-electron process,

 significantly limiting the reaction kinetics and requiring a catalyst with high rates and selectivities.

48 The process has been extensively studied using various supported nickel catalysts.

48,49 CO2 conversions of >95%,

 with the methane selectivity going up to 100% at temperatures of 700 K,

 have already been achieved.

49 However,

 for industrial commercialization,

 this process is only viable when the H2 is produced from renewable energy and the CO2 comes from cheap accessible waste streams.

10,49 As mentioned above,

 95% of the worldwide H2 production,

 however,

 comes from steam methane reforming,

 leading to a problematic flawed loop.

 Furthermore,

 the current cost for CO2 capture,

 separation and purification from waste streams is too high.

 Both reasons make this process economically unfeasible.

49

#7.1
The selective hydrogenation of CO2 to methanol,

 on the other hand,

 is a process that is currently operated on an industrial scale.

 The annual worldwide production of methanol is estimated to be around 70 M metric tonnes (2015).

 The most common commercial catalyst is copper supported on high surface area alumina (often promoted with zinc oxide).

47 The relevant reactions for the selective hydrogenation of CO2 are:50 CO2(g) + H2(g) → CO(g) + H2O(g) ΔH° = +40.9 kJ mol−1 (R5) CO(g) + 2H2(g) → CH3OH(g) ΔH° = −90.8 kJ mol−1 (R6) CO2(g) + 3H2(g) → CH3OH(g) + H2O(g) ΔH° = −49.9 kJ mol−1 (R7) While the overall reaction (reaction (7)) of CO2 hydrogenation to methanol is exothermic (ΔH° = −49.9 kJ mol−1),

 the rate determining step is the activation of CO2 in the reverse water–gas shift (RWGS) reaction,

 i.

e.

reaction (5).

 Obviously,

 doping metals that function as catalysts in the RWGS reaction will promote CO2 hydrogenation.

50 As a result,

 much effort is still focused on investigating the efficacy of Cu-based catalysts promoted with Pd and Ga,

51 with the fundamental material challenge centring on the fact that,

 generally,

 CO2 and H2 will only react at high temperatures with multicomponent heterogeneous catalysts.

24

One of the main drawbacks of the selective hydrogenation of CO2 to methanol in the above case is the production of water as a by-product (see reaction (7)).

 A third of the H2 is thus converted to water compared to the complete conversion to methanol when starting from syngas (see reaction (6)).

 Furthermore,

 the thermodynamics for methanol production from H2 and CO2 are not as favourable as those for the production from syngas (cf.

reactions (6) and (7)).

51 Therefore,

 on an industrial scale,

 methanol production usually relies on syngas in a 3 to 1 ratio from SMR (reaction (2)),

 while CO2 is added to deal with the excess H2 in the feed (compared to reaction (6)),

 and finally the produced water (reaction (7)) is recycled via the #%water–gas shift reaction (the reverse reaction of reaction (5)).

Nevertheless,

 to conclude,

 we can state that,

 currently the selective hydrogenation of CO2 with H2 into methanol is the most – if not to say only – industrially successful traditional process for the direct reforming of CO2 into chemicals and fuels.

#8
 2.2.3. CO2 + H2O: artificial photosynthesis

Although there is no real traditional approach for the combined conversion of CO2 and H2O,

 we present here the main overall reactions of interest for the combined conversion of CO2 and H2O,

 mostly for the sake of completeness and because of their interest to the discussion of novel technologies (see Sections 3 and 4): CO2(g) + H2O(g) → CO(g) + H2(g) + 1/2O2(g) ΔH° = +525 kJ mol−1 (R8) CO2(g) + 2H2O(g) → CH3OH(g) + 3/2O2(g) ΔH° = +676 kJ mol−1 (R9) These are clearly the most endothermic overall reactions described in this section,

 partially explaining the absence of a traditional (thermocatalytic) reforming approach.

 Fig.

 4 illustrates that the same high temperatures are needed for this reaction as for the pure CO2 splitting,

 while obtaining somewhat lower energy efficiencies.

 The highest energy efficiency (40%) is obtained at 3300 K together with a conversion of 60%.

 At higher temperatures,

 the energy efficiency decreases to 25% at 5000 K for a total conversion.

 Fig.

 4 Calculated theoretical thermal conversion (left axis) and corresponding energy efficiency (right axis) as a function of temperature for the conversion of CO2 and H2O into H2, CO and O2.

 Nevertheless,

 a process involving the reaction of CO2, H2O,

 O2 and CH4, called tri-reforming,

 is gaining quite some interest.

24 The concept,

 proposed by Song et al.

,31 involves a synergetic combination of dry reforming,

 steam reforming and the partial oxidation of methane in a single reactor,

 which can produce syngas in desired ratios (1.5–2.0),

 while eliminating carbon formation,

 as demonstrated for a fixed bed flow reactor at 1123 K over supported nickel catalysts.

31

#9
 3. Novel CO2 conversion approaches

It stands without doubt that the efficient conversion of CO2 to useful molecules presents an important challenge and a great opportunity for chemists today.

 Due to the inability of the traditional thermal approaches to address the worldwide CO2 and energy challenge,

 several promising novel technologies are under development.

 Plasma technology is one such technology,

 but before elaborating on this specific technology in more detail,

 first,

 a summary of its main ‘frenemies’ in this domain is given.

 For each technology,

 first a brief explanation of the working principles and current achievements is given,

 followed by the major advantages and challenges.

 From this section,

 it will become clear that there is,

 indeed,

 fierce competition in the quest to find the most effective and efficient CO2 conversion technology with the potential to be used on an industrial scale.

 It should be noted that only technologies for CO2 conversion are described here.

 For other (in)direct applications and fixation technologies,

 we refer to other reviews.

12–19
3.1. Electrochemical conversion

We kick off our discussions with one of the closest competitors to plasma technology,

 i.

e.

 the electrochemical conversion or reduction of CO2. This closeness derives from the fact that both technologies rely on the use of (renewable) electrical energy,

 whereas most of the other novel technologies only take direct advantage of renewable energy,

 i.

e.

 the sun,

 either based on its focused radiation heat or its emitted photons.

 Although significant technical and catalytic advances are still required for its large-scale use,

 electrochemical conversion is becoming a mature technology for H2O splitting.

 For CO2 reduction,

 on the other hand,

 several important challenges remain.

7,45,52–55

#9.1
The electrochemical %%valorization of CO2 is an innovative technology,

 in which electrical energy is supplied to establish a potential between two electrodes,

 allowing CO2 to be transformed into value-added chemicals under mild conditions.

7,55 This transformation can occur through a wide variety of pathways,

 which are typically strongly affected by the experimental conditions.

 The electrochemical reduction of CO2 can proceed through two-,

 four-,

 six- and eight-electron reduction pathways in gaseous,

 aqueous and non-aqueous phases in different cell and electrode configurations.

7,53Fig.

 5 shows the three main cell types.

 Fig.

 5(a) and (b) illustrate the principle of a solid proton conducting electrolysis cell (SPCEC) for the combined conversion of CO2 and H2O,

 and of a solid oxide electrolysis cell (SOEC) that could be used for either the pure or combined conversion of CO2 and H2O,

 respectively,

 while a typical alkaline electrolysis cell for water splitting is shown in Fig.

 5(c).

 The catalyst and/or electrode materials,

 the reaction medium,

 electrolyte solution,

 buffer strength,

 pH,

 CO2 concentration and pressure as well as the reaction temperature all influence and determine the wide variety of products that can be obtained.

53 The major reduction products obtained include carbon monoxide (CO),

 formic acid (HCOOH) or formate (HCOO−) in basic solution,

 formaldehyde (CH2O),

 methanol (CH3OH),

 oxalic acid (H2C2O4) or oxalate (C2O42−) in basic solution,

 methane (CH4),

 ethylene (C2H4) and ethanol (C2H5OH).

7,45,53
Fig.

 5 Principles of a solid proton conducting electrolysis cell (SPCEC) (a),

 solid oxide electrolysis cell (SOEC) (b) and an alkaline electrolysis cell (c) for the conversion of CO2 and/or H2O.

There are a number of reasons why the electrochemical reduction process stands out from the crowd; for instance,

 the process is controllable by several reaction parameters,

 including the electrode potential and temperature.

#9.2
7,45,52–54 Furthermore,

 a wide variety of valuable products can be made,

 either in mixtures or more importantly in their pure form.

 For example,

 besides the direct electrochemical reduction of CO2 to methanol,

 it is also possible to produce CO and H2 at the cathode in a H2/CO ratio close to 2, while at the anode,

 a valuable pure oxygen stream is generated (see Fig.

 1–5(b)).

45 Another advantage is that electrochemical conversion can make use of a wide variety of (intermittent) renewable electricity sources,

 i.

e.

 more than just solar energy.

53 Finally,

 the electrochemical reaction systems are compact,

 modular,

 on-demand and thus easy to utilize for small or large scale-up applications.

53

The accomplishments to date in the electrochemical reduction of CO2 have been encouraging,

 and the potential rewards are enormous.

7 Nevertheless,

 several challenges remain,

 such as the high %%overpotential,

 which is the difference in electrode voltage between the theoretical thermodynamic and actual real-world values to drive a reaction;52,54 the low solubility of CO2 in aqueous solutions;52 the formation of product mixtures,

 thus requiring expensive separation steps;52 fouling and catalytic deactivation of the electrodes by impurities,

 reaction intermediates and by-products;7,52,54 the instability of the electrode material;7 the low Faradaic efficiencies,

 current densities and high energy consumption;52,53 the kinetic barriers leading to low efficiencies;53,54 and the non-optimized electrode/reactor and system design for practical applications.

53 In general,

#9.3
 it is recognized that the single biggest challenge is the low performance of the electrocatalysts,

 due to low activity,

 low selectivity and most importantly insufficient stability.

 The reported stability tests in the literature are only in the order of,

 or below,

 100 hours,

 while long-term tests are non-existent to date.

53 This makes the development of stable electrocatalyst materials with high activity and selectivity the main priority for this technology.

7,53,56

It seems that despite many advances and successful proof-of-concepts being reported,

 the maturity of electrochemical CO2 reduction technology is still far from reaching the requirements for commercialization,

 due to the several remaining major technological challenges,

 as listed above.

7,52,53 Particularly for industrial-scale implementation,

 the low catalyst stability seems to be the major limitation.

53 As a result,

 no electrocatalysts developed to date for the reduction of CO2 would be deemed useful for a large-scale system.

54 As stated by Qiao et al.

,53 “With continued and extensive efforts focused on developing innovative composite and nanostructured catalyst materials to overcome the challenges of insufficient catalytic activity,

 product selectivity,

 and catalytic stability,

 the technology of CO2electroreduction will become practical in the near future”.

 Hence,

 to successfully achieve the transformation of CO2 to liquid fuels and useful chemicals,

 new methods and approaches for activating the CO2 molecule at lower overpotentials are required.

7 In the first instance,

 novel electrodes enabling operation at current densities close to commercially available H2O electrolyzers have to be developed,

 for which solid oxide electrodes appear to be suitable candidates.

52 Furthermore,

 a better understanding of the mechanistic role of metal and metal oxides in the reduction process is needed to open the possibility to design electrodes with certain compositions.

52 To conclude,

 efforts to optimize system designs and at the same time to develop durable catalysts still need to be carried out.

53 However,

 the final grand question remains: can all of this be done with inexpensive earth-abundant metals?54

@@@
#10
 3.2. Solar thermochemical conversion

Another technology,

 which has recently made several huge leaps forward,

 is the solar thermochemical conversion of CO2. There are several ways to reduce CO2 with the assistance of renewable solar energy,

 with those using direct solar light irradiation probably the most effective methods because there is no additional extra energy required and no negative influence on the environment.

57 Two forms of direct solar energy conversion can be distinguished: (i) thermal conversion – described here – where work can be extracted after sunlight is absorbed as thermal energy and (ii) quantum conversion – described in the next section – where the work output can be taken directly from the light absorber (e.

g.

 a semiconductor,

 molecule or organic compound).

58 For solar thermochemical conversion,

 concentrated solar radiation is used – in the form of high-temperature heat – as an energy source to drive the highly endothermic reactions.

The single step thermal dissociation of CO2 (or H2O) is impeded by the need to operate at high temperatures (>2500 K),

 as demonstrated in Fig.

 2 above,

 and the need for effective separation techniques to avoid ending up with an explosive mixture of CO/O2 (or H2/O2).

58,59 Multi-step thermochemical cycles using metal oxide redox reactions bypass the separation problem and,

 in addition,

 they allow operation at relatively moderate temperatures.

 More specifically,

 as shown in Fig.

 6, solar processes involving heat at ≥1500 K enable a two-step thermochemical cycle using metal oxide redox reactions for CO2/H2O-splitting.

58,59 The first – endothermic – step is the solar thermal reduction of the metal oxide MOox (where M is e.

g.

 Ce,

 Zn,

 or Fe)60 to the metal or to the lower-valence metal oxide MOred.

 The second – nonsolar – exothermic step is the oxidation of the reduced metal oxide with CO2 and/or H2O to form CO and/or H2, allowing the (re)oxidized metal oxide to be reused/recycled for the first step.

58,59 In general,

 two cycle categories can be considered: volatile and non-volatile.

 Non-volatile cycles utilize metal oxides,

 which remain in the solid state during reduction,

 while volatile redox cycles consist of metal oxides,

 which undergo gas–solid phase transitions.

 The volatile reactions appear more favourable,

 but the volatile products must be quenched rapidly to avoid recombination,

 and to date this issue has not been solved in an energetically efficient fashion.

59 For the non-volatile cycles,

 cerium oxide (ceria,

 CeO2) has emerged as a highly attractive redox active material choice for two-step thermochemical cycling.

60,61 Another promising pathway,

 which operates at lower temperatures than ceria,

 is the exploration of doped perovskite oxides.

62
Fig.

 6 Schematic of the two-step solar thermochemical cycle for CO2 and H2O splitting based on metal oxide redox reactions.

The main advantage of the solar thermochemical conversion of CO2 is obviously the direct use of solar energy.

 Concentrating solar technologies,

 which are currently applied commercially for large-scale (megawatt) power generation,

 can be coupled to high-temperature thermochemical reactors with the potential to achieve high solar-to-fuel energy conversion efficiencies and,

 consequently,

 the potential to produce solar fuels on a large scale and at a competitive cost.

58 To date,

 solar flux concentration ratios exceeding 2 MW m−2 are attainable with large-scale solar tower and dish systems.

 Solar thermochemical applications,

 although not as far developed as solar thermal electricity generation,

 employ the same solar concentrating infrastructure,

 with the solar reactor positioned at the focus of the solar tower (for megawatt centralized applications) or solar dish (for kilowatt decentralized applications).

58 A recent comprehensive review of solar concentrating technologies for thermal power and thermochemical fuel production was given by Romero et al.

63 Consequently,

 these cycles inherently have the potential to realize a greater theoretical efficiency than methods using energy vectors or a small part of the solar spectrum and are,

 in addition,

 conceptually simpler.

62,64 This potential to achieve high solar-to-fuel energy conversion efficiencies is primarily related to the fact that solar thermal processes inherently operate at high temperatures and utilize the entire solar spectrum,

 and,

 as such,

 provide a thermodynamically favourable path to the production of solar fuels.

58,59 A thermodynamic analysis based solely on the material properties of e.

g.

 CeO2 indicated that efficiency values in the range of 16–19% could be attainable,

 even in the absence of sensible heat recovery.

 These values are close to the 20% efficiency that is likely to be needed for solar fuels to be considered cost competitive,

65 as will be discussed in more detail in Section 6.3.

Although significant advances have been made in the field of solar thermochemical CO2 conversion technologies using metal oxides,

 a lack of fundamental research into the behaviour of the metal oxides under the high-temperature conditions present in these cycles has hampered the development of materials.

 Basic questions relating to oxygen transport,

 surface chemistry,

 structural changes vs.

 redox reactions,

 materials’ synthesis methods,

 the effects of thermochemical cycling on the material and the role of supports still have to be addressed.

66 Furthermore,

 despite its favourable thermodynamics,

 both the efficiency and the cycling rates in the reactor can be largely limited by thermal losses,

 resulting from poor conductive and radiative heat transfer across the porous metal oxide structure.

58 Finally,

 the thermochemical conversion rates are higher than,

 for example,

 the photocatalytic rates,

 but although conceptually simple,

 focusing lenses for sunlight and high-temperature reactors incur high initial investment costs.

60

Solar thermochemistry has clearly emerged as a viable path to utilize concentrated solar technology – currently applied commercially for large-scale power generation – for the conversion of CO2 (and H2O) into CO (and H2).

 Also,

 solar thermochemical cycles for the conversion of CO2 and H2O via the metal oxide redox reaction have favourable thermodynamics,

 but the ultimate factor dictating commercial viability is a high solar-to-fuel energy conversion efficiency,

 and to date efficiencies above 10% are still pending experimental demonstration with robust and scalable solar reactors.

58,59,62 The discovery of new materials with large oxygen exchange capabilities at moderate temperatures and their implementation in efficient solar reactors are thus essential.

 Additionally,

 rapid chemical kinetics and material stability over thousands of cycles must be demonstrated for each material considered.

59,67 This is the second key to achieving market viability,

 because materials must remain active for many thousands of redox cycles in order to avoid the high costs that would be associated with frequent replacement.

 As such,

 commercial success is again predicated upon finding appropriate materials composed of earth-abundant elements that can operate at lower reduction temperatures than current systems,

 together with sufficient activity to achieve high process efficiency.

62

]XXX

------------------------------------------ [resource] 20200526_153656
#%Plasma-Driven Catalysis	keyword	青２
%%flexibility to be scaled up and down	notice	緑４
#2	location number	青２ / オレンジ色１

1	([^\d])(\.|\,)	$1$2\n\n

/ ------------------------------------------ [resource] 20200526_153656 /