https://pubs.rsc.org/en/content/articlelanding/2017/cs/c6cs00066e#!divAbstract

M-47

=========================[ 20200601_123641
#1
 Plasma technology – a novel solution for CO2 conversion?

Abstract

CO2 conversion into value-added chemicals and fuels is considered as one of the great challenges of the 21st century.

 Due to the limitations of the traditional thermal approaches,

 several novel technologies are being developed.

 One promising approach in this field,

 which has received little attention to date,

 is plasma technology.

 Its advantages include mild operating conditions,

 easy upscaling,

 and gas activation by energetic electrons instead of heat.

 This allows thermodynamically difficult reactions,

 such as CO2 splitting and the dry reformation of methane,

 to occur with reasonable energy cost.

 In this review,

 after exploring the traditional thermal approaches,

 we have provided a brief overview of the fierce competition between various novel approaches in a quest to find the most effective and efficient CO2 conversion technology.

 This is needed to critically assess whether plasma technology can be successful in an already crowded arena.

 The following questions need to be answered in this regard: are there key advantages to using plasma technology over other novel approaches,

 and if so,

 what is the flip side to the use of this technology? Can plasma technology be successful on its own,

 or can synergies be achieved by combining it with other technologies? To answer these specific questions and to evaluate the potentials and limitations of plasma technology in general,

 this review presents the current state-of-the-art and a critical assessment of plasma-based CO2 conversion,

 as well as the future challenges for its practical implementation.

#2

1. Introduction
Environmental and energy applications of low temperature plasmas are gaining increasing interest worldwide.

 The central research question is whether plasma-based solutions can yield a valuable alternative to existing thermal processes and whether they can compete with other novel gas conversion technologies.

 Nowadays,

 the conversion of CO2 into chemicals and fuels is a hot topic.

 The worldwide transition to renewable energy gives plasma processes a clean electricity source,

 and due to their high operation flexibility,

 plasmas are very suitable for storing this intermittent renewable energy in a chemical form,

 i.

e.

 as fuels and chemicals.

1.1. CO2 mitigation and valorisation
Throughout history,

 the use of natural resources has played a major role in the rapid development of the human race.

 Among these resources,

 fossil fuels in particular have contributed to a fast and unprecedented development in human society.

 Still,

 this comes with a great cost,

 since burning fossil fuels leads to the emission of large amounts of the greenhouse gas CO2. Because these anthropogenic CO2 emissions outpace the natural carbon cycle,

 atmospheric CO2 concentrations have been increasing from 280 ppm since the beginning of the industrial revolution to 400 ppm in 2014.1 With high certainty,

 it can be said that it is this increase that has led to the current adverse global environmental climate changes,

1 which have a growing detrimental effect on our climate and environment,

 and that represent a severe threat to our current society and future generations in general.

2–5

Therefore,

 the conversion of this main greenhouse gas into value-added chemicals and liquid fuels is considered as one of the main challenges for the 21st century.

1,2 The aim is not only to tackle climate change,

 but also to provide an answer to our dependence on fossil fuels.

 As stated by Goeppert et al.

,6 “Whether humankind uses up most of the fossil fuel resources (combined with carbon capture) or uses increasingly alternative energies,

 the need for transportation fuels and materials that we currently obtain from petroleum and natural gas will remain.

 With increasing population,

 products based on carbon from plastics to medicines will also be required in increasing quantities.

 In order to fulfil the demand for carbon-based products,

 CO2will have to be recycled in an anthropogenic version of nature's own carbon cycle.

 Carbon capture and recycling (CCR) will capture CO2from any source,

 and eventually mainly from the atmosphere,

 and recycle it to new materials and fuels using any alternative energy source.

”

Utilization of this waste and converting it into a new feedstock not only complies with the framework of sustainable and green chemistry7,8 but also fits within the ‘cradle-to-cradle’ concept.

9 By generating useful products out of CO2 we create the possibility to effectively close the carbon loop.

 This has already resulted in a booming interest in technologies that can convert CO2 into value-added products,

10–12 since they can effectively convert waste into new feedstocks following the cradle-to-cradle principle.

9 Besides chemical conversion,

 which is the principle focus of this review,

 CO2 also has other applications in the field of carbon dioxide capture,

 storage and utilization,

 such as its fixation and technological utilization,

 for these and other processes,

 as well as in carbon capture,

 for which we refer to several existing reviews in the literature.

12–19

Besides the traditional thermal CO2 conversion,

 several alternative technologies are being investigated,

 such as electrochemical,

 solar thermochemical,

 photochemical and biochemical pathways,

 either with or without catalysts,

 as well as all their possible combinations.

 Their advantages and disadvantages are briefly discussed herein,

 as they form the context for a novel approach considered to have great potential in recent years,

 which is the approach based on (non-thermal) plasma.

20,21 Several options are being investigated in this regard,

 including both pure CO2 splitting into CO and O2, as well as the reaction with other gases,

 like CH4 (dry reforming of methane),

 H2 (hydrogenation of CO2) or H2O (artificial photosynthesis),

 aiming for the production of syngas and valuable oxygenates,

 such as methanol,

 formaldehyde and formic acid.

#3
1.2. Solar fuels
The important difference between the traditional thermal conversion approaches and the emerging technologies is their independence of burning fossil fuels to provide the necessary thermal heat to drive reactions.

 More precisely,

 biochemical pathways rely on the natural photosynthesis process to convert light (either natural or artificial) into biomass,

 which can then be harvested and further processed.

 Other emerging technologies,

 such as the solar thermochemical and photochemical processes rely on direct solar energy.

 The average solar flux striking the earth's surface is 175 W m−2, which represents more energy striking the earth's surface in two hours,

 i.

e.

 640 EJ,

 than the worldwide energy consumption from all sources combined in 2008, i.

e.

 514 EJ.

22 The solar thermochemical process makes use of concentrated solar heat,

 while the photochemical process relies on the energy of photons.

 Ultimately though,

 the electrochemical and plasmachemical processes rely on electricity.

 Fig.

 1 gives an overview of the different novel technologies and their principal use of renewable energy for the conversion of CO2 in a carbon neutral cycle.

The reliance of electrochemical and plasmachemical conversions on electricity at first seems to limit their use as a greenhouse gas mitigation technology,

 since currently,

 producing electricity generally results in CO2 emissions.

 This idea though could not be further from the truth due to the worldwide transition to renewable energy sources,

 such as solar and wind energy.

 In 2014, the estimated renewable energy share of the global final energy consumption was already 19.2%,

 while by the end of 2015, the estimated renewable energy share of global electricity production was 23.7%.

23 It is even at such a stage that the large-scale adoption of these renewable energy sources poses a challenge for the efficient storage and easy transport of the electricity produced,

 i.

e.

 not only regarding the need for peak shaving,

 but more importantly the need for technologies to follow the irregular and at times intermittent supply of renewable electricity in a flexible way.

 While storage in batteries is possible,

 it is less efficient than chemical storage in fuels.

24 Such fuels,

 often referred to as carbon neutral fuels or solar fuels,

 offer a much higher gravimetric and volumetric energy storage capacity,

 have much higher energy densities than electrical storage techniques and they match the existing worldwide liquid fuel infrastructure.

12,24

In the first instance,

 the reactions in which CO2 is involved can be divided into two categories: the production of chemicals and the production of fuels.

 The latter is considered as the most suitable target for the conversion of large volumes of CO2 since its market size is 12–14 times larger than the former.

 One of the most interesting compounds is methanol,

 which is positioned exactly in the middle of these two categories,

 being at the same time a raw chemical and a fuel,

 used in both combustion engines and fuel cells.

25

To achieve the transformation of CO2 into value-added chemicals or fuels,

 the reactions that are of greatest interest involve the conversion of CO2 with a %%co-reactant that acts as a hydrogen source (like CH4, H2 or H2O).

 Due to the existing infrastructure,

 liquid products are preferable to gases,

 for most applications at least.

 Two approaches can be considered to achieve this: the indirect oxidative pathway and the direct oxidative pathway.

 The main product of the former is syngas,

 a mixture of H2 and CO,

 which can be converted to almost any commercial bulk chemical or fuel in a second – albeit very energy intensively – step through methanol and/or Fischer–Tropsch synthesis.

10 In this case,

 it is of great importance to have a high degree of control over the H2/CO ratio to be able to steer the synthesis towards the desired products.

26 The %%direct oxidative pathway,

 on the other hand,

 tries to eliminate the energy-intensive middle man by converting the reactants immediately into hydrocarbons,

 short-chain olefins (e.

g.

 ethylene and propylene) and oxygenated products (e.

g.

 methanol,

 formaldehyde,

 dimethyl ether and formic acid).

Liquid products are more attractive over gaseous hydrogen,

 since – while in theory a ‘Hydrogen Economy’27 would be very attractive – the latter has a number of serious drawbacks due to its physico-chemical properties.

28 Furthermore,

 the infrastructure needed to safely transport,

 store and dispense hydrogen would be very expensive to roll out,

 while liquid chemicals match the already existing worldwide fuel infrastructure.

12,24 Hence,

 especially in the transportation sector,

 a transition from liquid–fossil-fuel-derived products (e.

g.

 gasoline,

 diesel fuel,

 kerosene) to a renewable and sustainable liquid fuel is highly desirable.

 Again,

 methanol is one of the most interesting possible candidates to fulfil these requirements.

 It is the simplest liquid chemical containing only one carbon.

 Although to date it is almost exclusively produced from natural gas (and shale gas) for economic reasons,

 it can easily be obtained from several (future) carbon sources,

 incl.

 CO2, biomass,

 biogas and landfill gas.

 Therefore,

 it has been proposed as a key solar fuel for the above-mentioned anthropogenic carbon cycle under the framework of a ‘Methanol Economy’.

6

To be economically competitive with the existing structures,

 the efficient production of these solar fuels is critical during the quest to find an effective CO2 conversion technology with the potential to be commercialized on a large scale.

@@@
#5
 2. Traditional thermal CO2 conversion approaches

We first briefly discuss the existing traditional (mainly thermocatalytic) approaches used on an industrial scale.

 As such,

 this section will act as a comparison for the novel technologies under development.

 This section is subdivided into: (1) pure CO2 splitting and (2) CO2 conversion in combination with a co-reactant,

 i.

e.

 CH4, H2 or H2O.

2.1. Pure CO2 splitting

Thermal CO2 splitting has not been very effective to date.

 This is not surprising from a thermodynamic point of view; the carbon–oxygen bonds are relatively strong (783 kJ mol−1)29 and the Gibbs free energy of formation (ΔG° = −394 kJ mol−1)24 clearly shows that CO2 is a highly stable molecule,

 requiring a substantial energy input,

 optimized reaction conditions and active catalysts for any chemical conversion to take place.

 Neither the entropy (TΔS°) nor the enthalpy (ΔH°) term seem favourable for its conversion.

2 The overall reaction is written as: CO2(g) → CO(g) + 1/2O2(g) ΔH° = +283 kJ mol−1 (R1) Of course,

 the high value of ΔH° does not mean that its conversion is not feasible.

 Indeed,

 strongly endothermic chemical reactions can be found in a large number of industrial processes used worldwide,

 a classic example being the steam reforming of methane (SMR):24,31 CH4(g) + H2O(g) → CO(g) + 3H2(g) ΔH° = +206 kJ mol−1 (R2) This highly endothermic reaction has found worldwide use.

 In the fertilizer industry,

 the H2 is used for the production of ammonia,

 while in the gas industry,

 this reaction is responsible for 95% of the worldwide H2 production.

 This shows that there is no reason to dismiss CO2 splitting just because it is highly endothermic.

 Hence,

 a fair amount of research towards this reaction has already been conducted,

 of which an overview can be found in the work of Rayne.

29

It is,

 however,

 clear that,

 without actively removing one of the products (i.

e.

 CO or O2),

 the equilibrium of this reaction lies strongly to the left.

 Thus,

 thermal CO2 splitting is thermodynamically and energetically only favourable at very high temperatures,

 as can be seen in Fig.

 2. At 2000 K for instance,

 the reaction is not very efficient: we can easily estimate that ca.

 92 kJ mol−1 would be needed to heat 1 mole of CO2 from 300 to 2000 K.

 Furthermore,

 the reaction enthalpy is equal to 245 kJ mol−1 at 2000 K.

 Based on a conversion of 1.5% at this temperature,

 the energy cost for the total conversion is ∼7.9 MJ mol−1, yielding an energy efficiency of only 4.4% with respect to the reaction enthalpy of 283 kJ mol−1 at 300 K.

 On the other hand,

 ca.

 184 kJ mol−1 would be needed to heat 1 mole of CO2 to 3500 K,

 and at this temperature the reaction enthalpy is equal to 206 kJ mol−1. Hence,

 based on a conversion of 80% at this temperature,

 the energy cost of the total conversion is then only ∼602 kJ mol−1, yielding an energy efficiency of 47% with respect to the reaction enthalpy of 283 kJ mol−1 at 300 K.

 While the conversion continuing to increase,

 above 3500 K the energy efficiency starts to decrease.

 At 5000 K,

 the conversion is 100% but the energy efficiency is only 35%,

 as can be deduced from Fig.

 2.

 Thus,

 it is clear that the equilibrium production of CO and O2 varies from less than 1% at temperatures below 2000 K up to 45–80% at the temperature range 3000–3500 K.

29,30 Therefore,

 the most pertinent studies regarding thermal CO2 splitting involve membrane reactor systems.

 Nigara and Cales32 used a calcia-stabilized zirconia membrane and CO as the sweep gas.

 At a temperature of 1954 K,

 they were able to reach a conversion of 21.5%,

 whereas the equilibrium production was a mere 1.2% at the same temperature.

32 The overall conversion,

 however,

 was much lower due to the permeation of O2 through the membrane,

 whereby it recombined with the CO sweep gas to form CO2. Itoh et al.

33 employed an oxygen permeable yttria-stabilized zirconia membrane and used argon as the sweep gas.

 Unfortunately,

 despite the removal of oxygen through the membrane,

 conversions of only up to 0.5% were obtained for a maximum temperature of 1782 K.

 Fan et al.

34 used a solid oxide (SrCo0.5FeO3) membrane reactor and methane as the sweep gas.

 Conversions of up to 10% were found at a temperature of 1213 K,

 which are one to two orders of magnitude higher than what could be expected to be attained conventionally.

 Nonetheless,

 the feed gas was diluted with four parts of helium per one part of CO2, and when this is taken into account,

 an effective conversion of only 2% was actually reached.

To summarize,

 these studies have demonstrated the possibility of producing CO and O2 by the direct thermal splitting of CO2 – at lower temperatures than the equilibrium predictions – by means of the use of semipermeable membranes to extract oxygen.

 Nevertheless,

 the attained overall effective conversions of 0.5–2% are too low to be considered practical for successful application on an industrial scale.

Because to date none of the above-mentioned alternative approaches to split CO2 at lower temperatures have yet realized acceptable conversions and energy efficiencies,

 thermocatalytic CO2 splitting is currently not applied on an industrial scale.

 The reason for this is the high energy consumption and,

 in addition,

 the lack of effective techniques for separating CO and O2 at high temperatures to avoid ending up with an explosive mixture.

 Nevertheless,

 we presented this brief summary of the initial efforts regarding thermal CO2 splitting to support a complete understanding of the matter,

 and because this work has laid the foundations for one of the novel technologies,

 i.

e.

 solar thermochemical CO2 splitting,

 discussed later (see Section 3.2).

2.2. Conversion of CO2 with a co-reactant

Due to the inherent high energy consumption and derived low energy efficiency of thermocatalytic CO2 splitting,

 the only practical way to reform CO2 consists of using a co-reactant.

 Thermodynamically speaking,

 it is significantly easier to convert CO2 when it is paired with a co-reactant that has a higher,

 i.

e.

 less negative,

 Gibbs free energy.

24 Some suitable candidates are CH4 (ΔG° = −50.7 kJ mol−1) and H2 (ΔG° = 0 kJ mol−1).

 In essence,

 these hydrogen-bearing energy carriers give up their intrinsic chemical energy to promote the conversion of CO2.

As such,

 it is no surprise that the most widely investigated traditional processes to convert CO2 involve the reaction with either CH4 or H2. The former is one of the best known traditional processes for reforming CO2 into synthesis gas or syngas,

 which is a mixture of H2 and CO.

 The reaction with H2 is known as the Sabatier reaction,

 which is a well-known process to generate CH4 (and H2O).

 Additionally,

 the combination of CO2 and H2 can also be used to produce methanol through the methanol synthesis process.

 A final process of interest to mention is the combined conversion of CO2 and H2O,

 a technique for which there is no real traditional approach.

 Nevertheless,

 we briefly mention it here because water is an interesting co-reactant to pursue for the growing array of novel techniques.

 After all,

 H2O is not only the most ubiquitous and cheapest hydrogen source,

 compared to CH4 and H2, but converting CO2 in combination with H2O to produce value-added products using renewable energy would successfully mimic natural photosynthesis.

35,36 It is interesting to note that besides CH4, H2 and H2O,

 other possible hydrogen sources could also be considered,

 such as glycerol.

 The use of glycerol as a hydrogen donor has already been suggested and successfully implemented for different technologies,

 such as its use as a hydrogen donor (and green solvent) in catalytic transfer hydrogenation–dehydrogenation reactions of various unsaturated organic compounds;37 its use as a hydrogen donor for the production of CH3OH from CO2 in a hybrid enzymatic/photocatalytic approach38 and its use in the plasma-based reforming of glycerol towards syngas,

39 which also led to the suggestion of using glycerol as a hydrogen donor for the possible in situ trapping of oxygen during the plasmachemical splitting of CO2.40 However,

 in this review,

 the focus lies on the above-mentioned three most commonly used hydrogen sources CH4, H2 and H2O.

]XXX

------------------------------------------ [resource] 20200526_153656
#%Plasma-Driven Catalysis	keyword	青２
%%flexibility to be scaled up and down	notice	緑４
#2	location number	青２ / オレンジ色１

1	([^\d])(\.|\,)	$1$2\n\n

/ ------------------------------------------ [resource] 20200526_153656 /